## Slide 1
ROBOTICS FUNDAMENTALS
Session 01 / 04: Mechanical, Electrical Systems & Design How a robot becomes a real, functioning physical system.
Thursday, 10 September 2026 • 20:00 GMT+3 Online Interactive Workshop for Beginners & Makers
ROBOTICS MASTERCLASS • SESSION 01 / 04
Notes: PRESENTER NOTES: 1. Welcome & Energy: - "Good evening and welcome to Session 01 of Robotics Fundamentals!" - "Whether you are an engineering student, an enthusiast, or a maker, this workshop is designed for YOU." 2. The Session Goal: - "This is not a boring calculus lecture. We are here to understand how a robot actually becomes a working physical system—from the motors and bones to the batteries and code." 3. Logistics: - "Keep your chat window open! We will have live polls, design sprints, and Q&A throughout."

## Slide 2
What Actually Makes a Robot Move?
Strong & fast muscles that turn electrical currents into mechanical force.
A. THE MOTORS
C. THE SOFTWARE
The intelligent mind: Path planning, sensor feedback, and real-time control loops.
The power & nerves: Motor drivers, clean wiring, and batteries supplying peak surges.
B. THE ELECTRONICS
D. THE SKELETON
The rigid structure: Links, bearings, and gears that bear loads without flexing.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
INTERACTIVE POLL • 💬 DROP ANSWER IN CHAT
Notes: PRESENTER NOTES: 1. Audience Poll: - "Vote in chat: A, B, C, or D! Which part is the most critical for a great robot?" 2. The Big Reveal: - "Most people vote Software. But think about it: If your muscles are strong and your brain is a supercomputer, but your bones are made of wet spaghetti... can you sign your name with a pen?" - "Robotics is the harmony of all four."

## Slide 3
Robotics = Integration (The 4 Pillars)
The Physical Skeleton: Bones (Links), Hinges (Joints), and Gears. Gives the robot reach, strength, and stiffness.
01. MECHANICS
03. CONTROL
The Reflexes: The closed-loop math (PID) that keeps joints stable and stops shaking or ringing oscillations.
The Nerves & Power: Converts gentle microcontroller logic into heavy physical muscle power without brownouts.
02. ELECTRONICS
04. SOFTWARE
The Mind: ROS 2, computer vision, and mapping: 'Where am I, and what task do I execute next?'
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
SYSTEM PHILOSOPHY • 🧠 THE 4 PILLARS
Notes: PRESENTER NOTES: 1. Human Body Metaphor: - "Keep this metaphor in your head all evening: Skeleton, Nerves, Reflexes, and Mind." - "Real robotics engineering happens at the intersections."

## Slide 4
The Robotic System: Sense ➔ Decide ➔ Act
How does a machine become autonomous?
1. SENSE (Inputs):
Encoders, cameras, LiDAR, and current sensors measure reality.
2. DECIDE (Compute):
Computes error between target position and actual position.
3. ACT (Outputs):
Motor drivers push current to wheels and joints to correct the error!
⚡ Loop Rate: This happens 100 to 1,000 times every single second!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
CORE ROBOTIC LOOP • SENSE ➔ DECIDE ➔ ACT
Notes: PRESENTER NOTES: 1. Walkthrough the Loop: - "Sense, Decide, Act. If any one of these three steps breaks, the robot is blind, paralyzed, or out of control." 2. Speed Matters: - "A quadcopter drone must run this loop at 500 Hz (500 times a second) or gravity wins."

## Slide 5
Before Building: Three Simple Questions
01. WHERE REACH?
• How far must the arm stretch? • Working on a flat table (2D) or full 3D space? • Rule: Keep joints to the bare minimum needed!
• Lifting a 10g feather or a 2kg bottle of water? • What motor torque is required? • ⚠️ Don't forget: The arm must lift its OWN weight too!
• Will the battery die in 10 minutes? • Will 3D printed links bend like rubber? • Will loose gear teeth (backlash) destroy accuracy?
02. HOW HEAVY?
03. WHAT LIMITS?
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
FIRST PRINCIPLES • 📐 3 SIMPLE QUESTIONS
Notes: PRESENTER NOTES: 1. The First Principles: - "Notice what is NOT on this slide: 'What programming language should I learn?'" - "First define reach, payload, and physical constraints."

## Slide 6
The Closed Feedback Loop: What Happens Without Sensors?
OPEN LOOP (Blind Walking):
• Sending commands to motors without feedback.
• If a wheel slips on tile, the robot has NO IDEA it drifted off course!
CLOSED LOOP (Eyes Open):
• Encoders continuously report wheel revolutions.
• If motor slows under load, controller increases current instantly.
👉 Takeaway: Sensors turn dumb blind motion into smart, adaptable robotics!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
CONTROL THEORY • 🔄 OPEN VS CLOSED LOOP
Notes: PRESENTER NOTES: 1. Interaction: - "Close your eyes and try to walk 10 steps in a straight line. You will inevitably drift. That is open-loop control." 2. Encoders: - "Closing the loop with encoders is what separates an electric toy from a real robot."

## Slide 7
PART 01 MECHANICAL FUNDAMENTALS
Links • Joints • Degrees of Freedom • The 6 Axes of Motion
ROBOTICS FUNDAMENTALS • PART 01 / 06
SECTION 01 • MECHANICAL FUNDAMENTALS
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 01: Mechanical Fundamentals. How does geometry become movement?" 2. Takeaway: - "Understand links, joints, and why 6 axes are the magic number."

## Slide 8
Links & Joints: The Kinematic Chain
A robot arm is simply a chain of rigid bones and hinges:
• LINKS = The Rigid Bones
Beams, extrusions, and brackets that maintain fixed distance between joints.
• JOINTS = The Hinges & Sliders
The precise points where controlled motion occurs, powered by motors.
🔗 Kinematic Chain: Base ➔ Link 1 ➔ Joint 1 ➔ Link 2 ➔ Joint 2 ➔ Tool
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
CORE CONCEPT
CORE ANATOMY • 🔗 LINKS & JOINTS
Notes: PRESENTER NOTES: 1. Keep it Concrete: - "Look at your own arm: Shoulder = Joint 1, Upper arm = Link 1, Elbow = Joint 2, Forearm = Link 2, Wrist = Joint 3, Fingers = End-Effector."

## Slide 9
The Two Fundamental Joint Types
• Like an elbow, knee, or door hinge • Motion: Rotation around an axis (Angle θ in degrees) • 90% of robotic arms are built purely of Revolute joints!
REVOLUTE (R) — ROTATIONAL
SCARA ROBOT (R-R-P)
• 2 Revolute joints for superfast horizontal sweeps • 1 Prismatic vertical slider for pick-and-place • High speed, ultra-rigid vertical assembly.
• Like an elevator, syringe, or 3D printer rail • Motion: Pure straight sliding (Distance d in millimeters) • Powered by lead screws, timing belts, or rack & pinion.
PRISMATIC (P) — LINEAR
CARTESIAN (P-P-P)
• 3 Orthogonal sliding axes (X, Y, Z) • Used in 3D printers and CNC milling machines • Super simple kinematics (X=d1, Y=d2, Z=d3).
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
KINEMATICS • ⚙️ REVOLUTE VS PRISMATIC
Notes: PRESENTER NOTES: 1. Simplify Joints: - "Almost every joint in the universe is either a Hinge (Revolute) or a Slider (Prismatic)." - "Combine them, and you get Cartesian, SCARA, or articulated robot arms."

## Slide 10
What is Degrees of Freedom (DOF)?
DOF = Number of independent directions a robot can move.
• 1 DOF: A train on a straight track (Forward / Backward)
• 2 DOF: A computer mouse on a mousepad (X and Y)
• 3 DOF: A drone in air without turning (X, Y, Z translation)
• 6 DOF: Complete spatial freedom! Can reach ANY position (X, Y, Z) and ANY orientation (Roll, Pitch, Yaw)!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
DEGREES OF FREEDOM • 🌐 SPATIAL MOTION
Notes: PRESENTER NOTES: 1. The 6-DOF Goal: - "In 3D space, any rigid object has exactly 6 degrees of freedom: 3 to position it, and 3 to orient it."

## Slide 11
Engineering Truth: More DOF ≠ Better!
Every extra motor adds weight. Joint 1 at the base must now lift the heavy motor of Joint 2, 3, 4, and 5!
1. COMPOUNDING MASS
3. BACKLASH ACCUMULATION
0.5° of loose gear play in 6 consecutive joints compounds into a massive 15 mm wobble at the gripper!
Each joint requires a precision motor, driver, gearbox, bearings, encoder, and machined brackets.
2. MULTIPLIED COST
4. WIRING FATIGUE
Passing 30 copper wires through 6 twisting joints is the #1 cause of broken wires and field failures.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
ENGINEERING TRUTH • ⚠️ MORE DOF ≠ BETTER
Notes: PRESENTER NOTES: 1. The Golden Rule: - "Use the MINIMUM number of joints to accomplish the mission. If your 3D printer only needs 3 axes, do not build a 6-axis arm!"

## Slide 12
Real Robot Anatomy: Why 6 Axes?
Why is the 6-Axis Industrial Arm (KUKA / ABB / FANUC) the king of factory automation?
• AXES 1, 2, 3 (The Arm Base):
Position the wrist anywhere in 3D space (X, Y, Z).
• AXES 4, 5, 6 (The Spherical Wrist):
Orient the tool in any direction: Roll, Pitch, and Yaw!
👉 Result: Can weld a car door seam from any angle!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
INDUSTRIAL ROBOTICS • 🦾 WHY 6 AXES?
Notes: PRESENTER NOTES: 1. Industrial Arm Anatomy: - "Axes 1 to 3 are the crane: they put the wrist in position." - "Axes 4 to 6 are the hand: they orient the welding torch or spray gun."

## Slide 13
Audit This Robot: What Do You See?
01. Count Links
02. Identify Joints
03. Calculate DOF
04. Locate Motors
05. Spot Wire Stress
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
HANDS-ON AUDIT • 🔍 INSPECT THIS ROBOT
Notes: PRESENTER NOTES: 1. Interactive Exercise: - "Look at any robot in your lab or online. Break it down using these 5 lenses." - "Where do the wires bend? That's where it will fail in 6 months."

## Slide 14
PART 02 ACTUATION & MOTORS
Motors • Torque • Speed • Backlash • Choosing the Right Drive
ROBOTICS FUNDAMENTALS • PART 02 / 06
SECTION 02 • ACTUATION & MOTORS
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 02: Actuation and Power Transmission. The muscles of the robot!"

## Slide 15
Which Motor for Which Job?
• Cheap, simple 2-wire control • High speed, moderate torque • Perfect for mobile robot driving wheels.
BRUSHED DC + GEARS
STEPPER MOTOR (NEMA)
• Precise discrete steps (e.g. 1.8°/step) • High holding torque at low speed • The gold standard for 3D printers & CNCs.
• All-in-one: Motor + Potentiometer + Driver • Easy PWM angle control (0°-180°) • Great for small camera gimbals & grippers.
RC HOBBY SERVO
BLDC + PLANETARY GEARS
• Supreme power-to-weight density & efficiency • High speed, quiet, zero brush wear • Used in Boston Dynamics quadrupeds & drones.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
SELECTION MATRIX • ⚡ WHICH MOTOR TO PICK?
Notes: PRESENTER NOTES: 1. Quick Guide: - "Wheels? Geared DC. 3D printer? Stepper. High-performance arm? Brushless (BLDC)."

## Slide 16
Torque: The Shopping Bag Principle
Holding a 2 kg bag against your hip is easy. Now hold that exact same bag straight out horizontally: Your shoulder burns within seconds! The weight didn't change—the DISTANCE changed! Distance multiplies rotational effort.
TORQUE = FORCE × DISTANCE
THE 2× SAFETY FACTOR RULE
Beginner Mistake: 'My static math says 2 N·m, so I bought a 2 N·m motor.' Why it stalls: You forgot the arm's own weight, acceleration torque, and bearing friction! Always multiply static torque by 2.0×.
QUICK WORKED EXAMPLE
1 kg payload (~10 N) at 20 cm reach (0.2 m) = 2.0 N·m torque. At 40 cm reach (0.4 m) = 4.0 N·m torque (Doubled!).
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
PHYSICS LAW • 📐 TORQUE & LEVERAGE
Notes: PRESENTER NOTES: 1. Real-World Analogy: - "Have everyone in the audience imagine holding that shopping bag. That burning feeling in your shoulder is what your joint motor feels every second."

## Slide 17
A Motor is More Than Just Torque!
Rotational strength. Can it lift the payload from a dead stop?
TORQUE (N·m)
RESOLUTION (Counts/Rev)
How finely the encoder divides a circle. (e.g. 4096 pulses per turn).
Rotational velocity. How fast can the joint travel?
SPEED (RPM)
BACKLASH (Arcmin / Degrees)
Mechanical wiggle between gear teeth when reversing direction.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
PERFORMANCE SPECS • 📊 KEY MOTOR METRICS
Notes: PRESENTER NOTES: 1. Don't Just Look at Torque: - "A winch motor has tons of torque, but takes 10 minutes to turn once. You need the right balance of torque and speed."

## Slide 18
Resolution ≠ Accuracy ≠ Repeatability
THE ARCHER ANALOGY:
• RESOLUTION: The finest tick mark on the sight.
Can measure tiny moves, but doesn't guarantee hitting bullseye!
• ACCURACY: Hitting near the center on average.
• REPEATABILITY: Hitting the exact same spot 100 times in a row!
👉 Industrial Secret: Factories care more about REPEATABILITY than absolute accuracy. If an arm is repeatable, software can calibrate the offset!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
METROLOGY TARGET • 🎯 ACCURACY VS REPEATABILITY
Notes: PRESENTER NOTES: 1. Archer Metaphor: - "High resolution without repeatability is useless. Always check repeatability on robot datasheets."

## Slide 19
Backlash: The Loose Steering Wheel
The tiny clearance gap between gear teeth so they don't bind. When you reverse motor direction, the motor turns slightly before the output gear engages!
WHAT IS BACKLASH?
THE DEAD ZONE DANGER
Inside the backlash gap, the arm floats freely with ZERO resistance from the motor! Your controller becomes blind and the arm shakes.
HOW TO BEAT IT
• Timing belts with tensioners • Harmonic strain-wave drives (zero backlash!) • Dual output encoders placed after the gearbox.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
MECHANICAL DANGER • ⚠️ GEARBOX BACKLASH
Notes: PRESENTER NOTES: 1. Steering Wheel Analogy: - "Have you ever driven an old car where you turn the wheel 2 inches before the tires react? That is backlash."

## Slide 20
Which Motor Would You Choose? [VOTE]
MOTOR A
• Torque: 0.5 N·m • Speed: 3000 RPM • Price: €25 • High speed, low torque
• Torque: 10.0 N·m • Speed: 50 RPM • Price: €120 • Massive torque, slow
• Torque: 4.0 N·m • Speed: 1000 RPM • Price: €60 • Balanced specs
MOTOR B
MOTOR C
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
LIVE VOTE • 🗳️ CHOOSE YOUR MOTOR
Notes: PRESENTER NOTES: 1. Trick Question Reveal: - "Trick question! None of them until you know your task requirements!" - "Never fall in love with motor specs before defining your payload."

## Slide 21
PART 03 MECHANICAL DESIGN
Structure • Materials • Stiffness • Real-World Trade-Offs
ROBOTICS FUNDAMENTALS • PART 03 / 06
SECTION 03 • MECHANICAL DESIGN & STIFFNESS
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 03: Mechanical Design. The skeleton that bears the load."

## Slide 22
The Load Path: Where Does Force Really Go?
01. THE MOTOR
• Generates spinning torque only! • ⚠️ NOT built to hold bending side weight! • Never bolt an arm directly to a motor shaft.
• The unsung heroes of robotics! • Soak up massive bending loads so the motor shaft doesn't snap. • Dual ball or cross-roller bearings.
• The rigid bones: Tubes and gussets. • If the arm bends even 2 millimeters under load, the gripper misses its target completely!
02. THE BEARINGS
03. THE STRUCTURE
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
STRUCTURAL ANALYSIS • 🧱 THE LOAD PATH
Notes: PRESENTER NOTES: 1. Human Bone Metaphor: - "Muscles generate pull, but bones and cartilage take the load. Separate torque generation from structural load bearing."

## Slide 23
Why Do Robot Arms Bend? (The Diving Board Effect)
Stand near the pool wall on a diving board: Feels solid as rock. Walk out to the tip: It bounces dramatically! Robot arms behave the exact same way.
THE DIVING BOARD ANALOGY
⚠️ THE L³ CUBIC DANGER!
Deflection ∝ (Force × Length³) / Stiffness. Length is CUBED (L³)! If you double the arm length (2×), it bends EIGHT TIMES as much (2³ = 8)! Small reach increases destroy stiffness.
THE TUBE SECRET
Use hollow square tubes or cylinders instead of solid flat bars! Material far from the center axis gives 10× more stiffness without added weight.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
PHYSICS LAW • 📏 CUBIC DEFLECTION (L³)
Notes: PRESENTER NOTES: 1. Explain L³ Simply: - "Double the reach = 8x the bend. That is why industrial robot arms look stocky and thick."

## Slide 24
Choosing Materials: What Should You Build With?
PLA (3D Print): Cheap & fast, but sags at 55°C
PETG / ABS: Tougher prints, great for brackets
ALUMINUM 6061: 20× stiffer than plastic! (Winner)
STEEL: Maximum strength, great for heavy base plates
CARBON FIBER: Featherweight rigidity, but expensive
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
MATERIAL MATRIX • 🔬 ALUMINUM VS PLA VS CF
Notes: PRESENTER NOTES: 1. Maker Strategy: - "3D print brackets on Friday night, but use aluminum tubes for long structural arms!"

## Slide 25
The Engineering Triangle: Pick Any Two!
HIGH PRECISION
• Sub-millimeter accuracy • Zero gear backlash • Machined joints & harmonic drives • Rigid steel rails
• Carbon fiber links • High power density motors • Featherweight agility • Fast acceleration
• 3D printed brackets • Hobby timing belts • Standard hardware fasteners • Under €300 budget
LIGHT WEIGHT
LOW COST
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
DESIGN TRADEOFF • ⚖️ THE TRIANGLE (PICK 2)
Notes: PRESENTER NOTES: 1. The Iron Law: - "You cannot build a NASA precision robot for 100 dollars. Great engineering is choosing the right compromise."

## Slide 26
What Happens When You Double the Reach?
• Payload: 1.0 kg • Joint Torque: 2.5 N·m (Small motor) • Tip Sag: 1.0 mm (Barely noticeable) • Settling Time: 0.15s (Rock steady!)
ARM A: 25 CM (COMPACT)
ROTATIONAL INERTIA (4×)
Inertia = Mass × Radius². Doubling arm length quadruples rotational resistance to stopping!
• Payload: 1.0 kg (Exact same payload!) • Joint Torque: 5.0 N·m (2× bigger motor) • Tip Sag: 8.0 mm! (8× worse sag!) • Settling: Shakes for 1.5s like tuning fork!
ARM B: 50 CM (2× DOUBLED!)
DESIGN TAKEAWAY
Keep your robot arms as short and compact as humanly possible! Every extra centimeter costs motor torque and stiffness.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
LEVERAGE COST • 💥 DOUBLING THE REACH
Notes: PRESENTER NOTES: 1. The Tuning Fork: - "When Arm B stops, it vibrates like a guitar string for 1.5 seconds. Always design arms compact."

## Slide 27
Design Challenge: Specify This Arm! [5-MIN]
• Payload: 2.0 kg • Reach: 60 cm (0.60 m) • Accuracy: < 1.5 mm • Budget: €400 total parts What material? What motor? What transmission?
CLIENT REQUIREMENTS
ROOKIE TRAPS
❌ Trap 1: 'Print the 60 cm arm in PLA!' (Will sag 12 mm!) ❌ Trap 2: 'Direct drive servo!' (Plastic gears strip instantly!)
WINNING PRO SPEC
• Hollow square aluminum tube links • NEMA 23 stepper with 15:1 planetary gearbox • Dual preloaded ball bearings on main pivot.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
DESIGN SPRINT • ⏱️ 5-MIN SPEC CHALLENGE
Notes: PRESENTER NOTES: 1. 3-Minute Sprint: - "Drop your choices in chat: Aluminum or plastic? Stepper or servo?"

## Slide 28
PART 04 POWER & ELECTRICAL
Voltage • Current • Batteries • The Dreaded Brownout Mystery
ROBOTICS FUNDAMENTALS • PART 04 / 06
SECTION 04 • POWER & ELECTRICAL
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 04: Power and Electrical Systems. A robot without power is an expensive paperweight."

## Slide 29
Electrical Fundamentals: The Water Pipe Analogy
VOLTAGE (Volts)
• Water Pressure in the pipe • Electrical push driving electrons • Higher Voltage = Higher maximum motor RPM (Speed)!
• Water Flow Volume per second • Actual amount of electrons moving • More Current = STRONGER MOTOR TORQUE (Strength)!
• Total Work Done (P = V × I) • Pressure × Volume = Power washing force! • 12V × 2A = 24 Watts continuous.
CURRENT (Amps)
POWER (Watts)
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
INTUITIVE ANALOGY • 🚰 THE WATER PIPE MODEL
Notes: PRESENTER NOTES: 1. Remember This: - "Voltage gives you SPEED. Current gives you TORQUE. Multiply them for Watts."

## Slide 30
The 4-Motor Trap: Why Robots Shut Down on Startup
• 1 Motor: 12V × 2A = 24 Watts • 4 Motors: 4 × 24W = 96 Watts • Beginner buys a '100W' power pack: 'Looks plenty!'
PAPER CALCULATION (96W)
THE COLLAPSE
The 100W battery pack cannot deliver 480W. Voltage crashes to 8V, and the robot instantly reboots!
• At 0 RPM, a motor is a direct short circuit! • Starting draws 5× stall current (10A per motor)! • 4 Motors × 10A = 40 AMPS (480 Watts) peak burst!
THE STARTUP SURGE (480W!)
GOLDEN POWER RULE
Always size batteries, wires, and fuses for PEAK SURGE, never for gentle average cruising speed!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
ELECTRICAL TRAP • ⚠️ THE 4-MOTOR TRAP
Notes: PRESENTER NOTES: 1. Real Competition Story: - "Robots reboot on the starting line because the 0.5-second acceleration spike trips the battery protection."

## Slide 31
Battery Runtime: Why Does 1 Hour Become 38 Mins?
• Battery: 12V × 10Ah = 120 Watt-Hours (Wh) • Robot draws: 120 Watts continuous • Ideal Runtime: 120 Wh ÷ 120 W = 1.0 Hour (60 mins)
THEORY (Watt-Hours)
THE 4 RUNTIME THIEVES
1. Usable Depth: Discharging lithium below 20% damages cells (lose 20% capacity). 2. Heat Sag: Fast discharge wastes energy as heat. 3. Regulators: DC-DC step-down converters waste 12%. 4. Sensors: LiDAR & Jetson draw steady base power.
THE 70% DERATING RULE
Always multiply theoretical paper runtime by 0.65× to 0.70× for real mission planning!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
ENERGY MATH • 🔋 BATTERY RUNTIME CALC
Notes: PRESENTER NOTES: 1. Field Truth: - "Sales sheet: 2 hours. Lab test: 42 minutes before safety shutoff. Plan accordingly."

## Slide 32
The Brownout Mystery: Why Did My Robot Reboot?
Motors demand high current (30A+) to overcome carpet friction and accelerate.
1. ACCELERATION BURST
3. REGULATOR DROPOUT
The 5V regulator dips to 4.2V for just 2 milliseconds. Microcontroller triggers reset!
Battery internal resistance causes terminal voltage to sag from 12V down to 9V.
2. VOLTAGE DROOPS
4. HOW TO FIX IT
• Isolate brain power rail from motor rail • Add 1000 µF bulk capacitor at motor drivers • Separate signal grounds to prevent noise.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
DETECTIVE STORY • 🕵️ THE BROWNOUT MYSTERY
Notes: PRESENTER NOTES: 1. Debugging Detective: - "'It worked on my desk!' On the desk, wheels spun freely. On carpet, friction triggered the brownout."

## Slide 33
PART 05 SOFTWARE & SIMULATION
Software Stacks • Free Tools • Firmware • ROS 2 Architecture
ROBOTICS FUNDAMENTALS • PART 05 / 06
SECTION 05 • SOFTWARE & SIMULATION
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 05: Software, Tools & Simulation. Where does code actually live in a robot?"

## Slide 34
The Robot Software Stack: Separation of Layers
High-level planning: Object detection (YOLO), SLAM mapping, speech recognition, and mission logic.
AI & AUTONOMY
MOTION PLANNING
Calculates smooth trajectories (Nav2, MoveIt) so arms and wheels move without hitting walls.
The telephone network: Lets modular software nodes communicate via Publish/Subscribe topics.
ROS 2 MIDDLEWARE
EMBEDDED FIRMWARE
Hard real-time C/C++ on microcontroller (STM32/ESP32) reading encoders and pulsing motor PWM pins.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
SYSTEM LAYERS • 🧠 THE ROBOT SOFTWARE STACK
Notes: PRESENTER NOTES: 1. Layer Rule: - "Never pulse motor pins from desktop Python, and never run heavy AI on an Arduino. Respect the layers."

## Slide 35
Your Free Robotics Starter Kit (Zero License Cost!)
Autodesk Fusion (Free Hobbyist) or FreeCAD. Model parts, check clearances, and export 3D STL files.
3D CAD MODELING
PHYSICS SIMULATION
Webots or Gazebo. Test navigation and obstacle avoidance in 3D worlds without paying for broken hardware!
KiCad (100% Free & Open-Source). Draw schematics and route real motor driver boards without paywalls.
CIRCUITS & PCBS
ROBOT MIDDLEWARE
ROS 2 (Humble / Jazzy). The industry framework used by NASA and autonomous car companies.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
OPEN SOURCE TOOLS • 🛠️ FREE STARTER KIT
Notes: PRESENTER NOTES: 1. Democratizing Robotics: - "You do not need $10,000 corporate licenses. Everything you need to build world-class robots is free."

## Slide 36
The Rookie Trap: Don't Confuse CAD, Sim & Reality!
IN CAD DESIGN
• The ideal fantasy world • Zero friction & infinite stiffness • Perfect zero-clearance bearings • Ambient temperature: 20.00°C!
• Physics is simulated • Friction is just an estimated number • ⚠️ Wheels never get dust or wires caught around axles!
• Screws vibrate loose • Batteries sag under load • Carpet has 3× more friction than tile • Real physical floor truth!
IN SIMULATION
IN REALITY
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
ROOKIE TRAP • ⚠️ CAD VS SIM VS REALITY
Notes: PRESENTER NOTES: 1. Quote: - "'Installing ROS doesn't make your robot autonomous—just like installing Photoshop doesn't make you Leonardo da Vinci!'"

## Slide 37
PART 06 FROM IDEA TO WORKING ROBOT
The Engineering Loop • Why Prototypes Fail • The Capstone Challenge
ROBOTICS FUNDAMENTALS • PART 06 / 06
SECTION 06 • FROM IDEA TO WORKING ROBOT
Notes: PRESENTER NOTES: 1. Section Intro: - "Part 06: Prototyping and Reality. This is where engineers are forged."

## Slide 38
The Real Engineering Loop: Failure is Step 5!
1. DEFINE: Specs, reach, payload, and budget limit
2. CAD MODEL: 3D assembly, check gear clearance
3. BENCH PROTOTYPE: 3D print brackets & wire drivers
4. TEST TO LIMITS: Load with 100% full payload on floor
5. THE BREAK 💥 ➔ 6. REDESIGN V2 IN METAL & WIN!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
ENGINEERING PROCESS • 🔄 THE 6-STEP CYCLE
Notes: PRESENTER NOTES: 1. Mindset: - "If your first prototype doesn't break, you didn't test it hard enough. Breaking on your workbench is how you find your real safety boundaries."

## Slide 39
"It Worked in CAD!" — Reality Has Entered the Room
Left: Pristine CAD rendering (Zero gravity, zero wire clutter) • Right: Physical reality (3D print layer lines, zip ties, hot glue, and real floor friction!) Always leave room for cables and tolerances.
REALITY CHECK • ⚡ PHYSICAL CONSTRAINTS
Notes: PRESENTER NOTES: 1. Relatable Humor: - "Every engineer laughs at this slide because every engineer has lived it. Leave room for cables from day one."

## Slide 40
Case Study: 3D-Printed V1 Failure ➔ Metal V2
• 100% printed in ABS plastic • Under 2 kg load, gear teeth sheared clean off! • Joint deflected 15° sideways without bearings.
WHAT FAILED IN V1
THE V2 REDESIGN
• Hardened steel planetary gears (15:1) • CNC aluminum pivot bracket with dual ball bearings • Easily holds 2.5 kg with zero deflection!
ENGINEERING LESSON
V1 failed so V2 could fly. Document your failure, calculate the missing margin, and engineer the fix.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
CASE STUDY • 🛠️ V1 FAILURE ➔ V2 REDESIGN
Notes: PRESENTER NOTES: 1. Don't Hide Failures: - "In your portfolio, document your failures and how you solved them. That is what top engineering companies hire for."

## Slide 41
Capstone Challenge: Campus Robot
• Mission: Autonomous book delivery on campus corridors
• Target Payload: 5.0 kg package capacity
• Cruising Speed: 1.0 m/s (Brisk walking pace)
• Target Runtime: 1.0 Hour continuous driving
• Environment: Flat indoor linoleum hallways
• Hardware Budget Limit: €300
👉 ASSEMBLE YOUR SPEC IN THE CHAT:
1. Drive: Differential 2WD + Caster vs 4WD Skid-Steer?
2. Motors: Geared DC vs Steppers vs Brushless?
3. Battery: 12V 5Ah vs 12V 10Ah LiFePO4?
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
CAPSTONE MISSION • 🚀 CAMPUS DELIVERY ROBOT
Notes: PRESENTER NOTES: 1. Team Sprint: - "You are the chief engineers. Drop your drive topology and battery choice in chat!"

## Slide 42
New Client Requirement: The 15° Ramp Twist! 🚨
Climbing a 15° slope adds 26% of robot weight as direct backward drag! Flat-ground motors will stall.
GRAVITY PULLS BACKWARD
WHEEL SLIP & TRACTION
Smooth plastic or omni-wheels will spin out without high-grip rubber treads on the incline!
BACKWARD FLIP & CURRENT
If the battery is mounted high/rearward, the robot flips backward! Climbing draws 3× current (runtime drops to 20m).
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
THE TWIST • 🏔️ 15° RAMP INCLINE CHALLENGE
Notes: PRESENTER NOTES: 1. The Lesson of the Ramp: - "One small change in terrain ripples through motor torque, battery runtime, tire material, and center of gravity."

## Slide 43
Session Summary: The 10 Rules of Robotics
1. Define task before buying motors 2. Minimize degrees of freedom 3. Always add 2× safety factor on torque
RULES 1 TO 3
RULES 7 TO 8
7. Size batteries for peak acceleration surge 8. Isolate computer power from noisy motors
4. Resolution on paper ≠ physical accuracy 5. Beware gear backlash—it ruins precision 6. Hollow aluminum tubes beat plastic 3D prints
RULES 4 TO 6
RULES 9 TO 10
9. Test with real physical loads, not just sim 10. Failure is step 5—build, test, break, and iterate!
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 • THURSDAY, 10 SEPT 2026
WORKSHOP RECAP • 📜 10 GOLDEN RULES
Notes: PRESENTER NOTES: 1. The Cheatsheet: - "Take a screenshot of this slide and put it above your workbench."

## Slide 44
DEFINE • DESIGN • BUILD TEST • BREAK • IMPROVE
THAT'S ROBOTICS. See you next Thursday for Session 02: Sensors, Perception & State Estimation! Thank you for attending! Let's open the floor for Q&A.
ROBOTICS FUNDAMENTALS • SESSION 01 / 04 COMPLETE
SESSION FINALE • ❓ OPEN Q&A SESSION
Notes: PRESENTER NOTES: 1. Inspiring Close: - "Define. Design. Calculate. Build. Test. Break. Improve. That is the true path of robotics." 2. Teaser: - "Next week in Session 02: We give our robot eyes and ears with LiDAR, depth cameras, and Kalman filtering." 3. Q&A: - "I'll now open the floor for questions! Drop them in the chat or unmute."